## Slide 2: Complex Event Detection – The Big Picture
Input: Streams of Simple Derived Events (SDEs)
Output: Complex Events (CEs)
    Collections of SDEs/CEs satisfying some pattern
    Patterns defined using a variety of contraints (temporal, spatial, logical,…)
    N. Giatrakos, E. Alevizos, A. Artikis, A. Deligiannakis, M. Garofalakis: Complex event recognition in the Big Data era: a survey. VLDB J. 29(1): 313-352 (2020)

## Slide 3: Motivating Example: Safe Robot Navigation in Smart Factory Scenarios
SDE Instances:
    Stopped
    Moving
    At Station Si (@Si)
    Rotating
    Goal: Reached Delivery Target
    Blocked: Wall/obstacle
    …
Pattern: SEQ(@Si, Moving, Rotating, Stopped, Blocked, Rotating)
within 5mins
CE: Delivery Failure
Aftermath: Delays in production line L
Credits: DFKI

## Slide 4: Raw Streams: Actual Input
Raw streams are not SDEs in the real world 
current_time | current_step | pos_x | pos_y | pos_z | rot_x | rot_y | … | rot_z | …
8.35 | 752 | -3.626 | 14.921 | 0.258 | 0.0987 | -0.0019 | … | 0.9951 | …
8.36 | 753 | -3.631 | 14.922 | 0.258 | 0.0979 | -0.0019 | … | 0.9951 | …
30.57 | 3382 | -7.473 | 23.746 | 0.258 | 0.8197 | -0.0012 | … | 0.5727 | …
38.31 | 3448 | -4.432 | 23.861 | 0.258 | 0.8235 | -0.0011 | … | 0.5671 | …
41.15 | 3704 | -7.446 | 23.866 | 0.257 | 0.9951 | 0.0006 | … | 0.0977 | …
41.12 | 3705 | -7.444 | 23.867 | 0.258 | 0.9952 | -0.0001 | … | 0.0972 | …

## Slide 5: Desiderata for SDE Extraction: Part I
Ground Truth - Labeled tuples  Simulations
Examples of actual SDEs
…used to train (NN) models
…used to tag unlabeled tuples from the application field
current_time | current_step | pos_x | pos_y | pos_z | rot_x | rot_y | rot_z | … | Label/SDE
8.35 | 752 | -3.626 | 14.921 | 0.258 | 0.0987 | -0.0019 | 0.0001 | … | stopped
8.36 | 753 | -3.631 | 14.922 | 0.258 | 0.0979 | -0.0019 | 0.0001 | … | stopped
30.57 | 3382 | -7.473 | 23.746 | 0.258 | 0.8197 | -0.0012 | 0.0015 | … | moving to Station2
38.31 | 3448 | -4.432 | 23.861 | 0.258 | 0.8235 | -0.0011 | 0.0013 | … | @ Station2
41.15 | 3704 | -7.446 | 23.866 | 0.257 | 0.9951 | 0.0006 | 0.0042 | …. | @ Station2
41.12 | 3705 | -7.444 | 23.867 | 0.258 | 0.9952 | -0.0001 | 0.0032 | …. | moving to Station3

## Slide 6: SSTRESED Version 1.0
Training Topic
Movement Streams
Learner
Weights Topic
Tagger/Classifier
SDEs
NN Weight Updates
Labeled Time Series - Simulations
Unlabeled Time Series - Application Field
Training Pipeline
SDE Detection Pipeline

## Slide 7: Desiderata for SDE Extraction: Part II
Support large scale applications – Big Data
  1000s of robots producing 100s of MB/min
  Rapid Continuous Model Training and Online SDE Detection
    High throughput : number of tuples being processed/tagged per time unit
    Low latency: amount of time a tuple remains in the Training/SDE detection pipeline
Solution: Scale-out all kinds of computation
  Multiple workers for the Training Pipeline
  Multiple workers for the SDE Detection Pipeline
  Parallel Processing: Key-based parallelization (Robot ID)

## Slide 8: SSTRESED Version 2.0

## Slide 9
Training Topic
Movement Streams
Learners
Parameter Server
Weights Topic
Tagger/
Classifier
SDEs
NN Weight Updates
Labeled Time Series @ Partition 1
Labeled Time Series @ Partition N
Unlabeled Time Series @ Partition 1
Unlabeled Time Series @ Partition M
…
Tagger 1
Tagger 2
Tagger m
…
…
Notes: The trajectory segmentor should deal with the variable input length issue.

## Slide 10: Desiderata for SDE Extraction: Part III
current_time | current_step | pos_x | pos_y | pos_z | rot_x | rot_y | … | rot_z | Label
8.35 | 752 | -3.626 | 14.921 | 0.258 | 0.0987 | -0.0019 | … | 0.9951 | stopped
8.36 | 753 | -3.631 | 14.922 | 0.258 | 0.0979 | -0.0019 | … | 0.9951 | stopped
10.01 | 888 | … | … | … | … | … | … | … | moving to Station2
30.57 | 3382 | -7.473 | 23.746 | 0.258 | 0.8197 | -0.0012 | … | 0.5727 | moving to Station2
35.88 | 3400 | … | … | … | … | … | … | … | moving to Station2
38.31 | 3448 | -4.432 | 23.861 | 0.258 | 0.8235 | -0.0011 | … | 0.5671 | @ Station2
41.15 | 3704 | -7.446 | 23.866 | 0.257 | 0.9951 | 0.0006 | … | 0.0977 | @ Station2
41.12 | 3705 | -7.444 | 23.867 | 0.258 | 0.9952 | -0.0001 | … | 0.0972 | moving to Station3
SDEs (not only CEs) are implicitly durative in the Training Pipeline…

## Slide 11: Desiderata for SDE Extraction: Part III
Required Output of the SDE Detection Pipeline…
Time_From | Time_To | SDE
8.35 | 8.36 | stopped
10.01 | 35.88 | moving to Station2
38.31 | 41.15 | @ Station2
41.12 | 45.85 | moving to Station3
… | … | …

## Slide 12: SSTRESED Version 3.0

## Slide 13: Movement Feature Vectors (MFVs) Micro-batches
speed | direction | acceleration
35 m/s | 76o | 40 m/s2
… | … | …
60 m/s | 85o | 55 m/s2
MFVs in micro-batch make up a Matrix |  | 
35 | … | 60
76 | … | 85
40 | … | 55
0.1 | … | 0.05
1 | … | 3
π/36 | … | π/16
Raw/Original MFVs
Derived MFVs

## Slide 14: Distributed SeTraStream –Segmentor View
…
O8
…
Oi
…
Candidate Div Point
SDE1
SDE2
W1l
W2l
W3l
Wr
O5
Short term change?
Long term change?
Robot OF
Robot Oi
Robot O1
Incoming micro-batches per Robot ID

## Slide 15: Distributed SeTraStream – Segmentation Rationale
…
T
O8
…
Oi
…
Candidate Div Point
SDE1
SDE2
W1l
Wr
O5
Dissimilar features?
If YES
σ thres
Incoming micro-batches per Robot ID
Similarity Metric
RV-coefficient (W, Wr)
Robot OF
Robot Oi
Robot O1

## Slide 16: Distributed SeTraStream – Tagging SDEs
…
…
Div Point
SDE1
SDE2
SDE3
Start of SDE4
End of SDE3
Robot OF
Robot Oi
Robot O1

## Slide 17: Distributed SeTraStream – Long-term Movement Change
…
T
O8
…
Oi
…
Incoming micro-batches per Robot ID
Candidate Div Point
SDE1
SDE2
W1l
W2l
W3l
Wr
O5
dissimilar features?
If NO
σ thres
Similarity Metric
RV-coefficient (W, Wr)
Robot OF
Robot Oi
Robot O1

## Slide 18: SSTRESSED Epilogue
1st Scalable Streaming Framework for SDE Detection
  Novel framework & architecture treats SDEs as first-class citizens
  Distributed processing across state-of-the-art Big Data Technologies
  1st to combine streaming semantic trajectory extraction and CER
More Applications
On-going work
  Complete implementation
  Enrich semantics (terrain images, map POIs etc)
  Trajectory compression before segmentation
  Wayeb[VLDBJ’22], EasyFlinkCEP [CIKM’21] Interoperability
Credits: MarineTraffic

## Slide 19: Thank you
Nikos Giatrakos
ngiatrakos softnet.tuc.gr
ngiatrakos athenarc.gr